## Slide 1: 2018 Steering System Design

## Slide 2: Steering Rack

## Slide 3: Last Year’s Setup
Functioned well
Ackermann and speed ratio could be increased
Heavy

## Slide 4: Design Goals/Constraints
Rack must mount on outside of the frame
Make lighter than previous
Keep handling parameters the same
We have to be able to make it
Keep cost down

## Slide 5: What decisions were made?
Aluminum rack
Same gearing
Carbon Fiber in Housing
Slightly less overall travel (less rack teeth)
Place bushings on outside
Lash adjustment

## Slide 6: Steering Column

## Slide 7: Last Year’s Setup
Compliance
Heavy

## Slide 8: Design Goals/Constraints
Simplify/reduce housing material
Reduce compliance
Look into shortening attaching frame members
Joints must run under acceptable angles

## Slide 9: What decisions were made?
Two shaft setup with double u-joint. Allows for Ackermann we want, simpler to constrain well
Use same kind of U-joints, shafts, quick release
Change from ball bearings to needle roller bearings
Make replacement quick release hex from aluminum

## Slide 10: Weight Savings
Steering Rack
Steering Rack: 1404g  746g = 658g
Support Material: 441g  46g = 395g
TOTAL = 1448 grams = 3.19 lbs
Steering Column
Steering Column: 617g  498g = 119g
Steering Housing: 296g  111g = 185g
Support Material: Save 91 grams